## Slide 1: Ch 4 Amplitude Modulations and Demodulations
ENGR 4323/5323
Digital and Analog Communication
School of Engineering
University of Central Oklahoma
Dr. Mohamed Bingabr

## Slide 2: Chapter Outline
Baseband vs. Carrier Communications
Double-Sideband Amplitude Modulations (DSB)
Amplitude Modulation (AM)
Vestigial Sideband Amplitude Modulations (VSB)
Local Carrier Synchronization
Frequency Division Multiplexing (FDM)
Phase-Locked Loop and Applications
NTSC Television Broadcasting System

## Slide 3: Baseband Vs. Carrier Communications
Baseband signals produced by various information sources and its original spectrum is not modified.
Baseband Communications: Baseband signals are transmitted without any modifications of its spectrum. By conversion process (Modulation), such signals are modified to facilitate transmission.
Carrier Communication: Communication that uses modulation to shift the frequency spectrum of a signal.
Purpose of Modulation:
  Ease of radiation.
  Reduce noise and interference.
  Multiplexing or transmission of several messages over a single channel.

## Slide 4: Type of Modulation
Analog Modulation: The original analog signal modulates one of the following parameters of a sinusoidal carrier of high frequency:
  Amplitude Modulation (AM)
  Frequency Modulation (FM)
  Phase Modulation (PM)
Angle Modulation
Analog modulation shifts the spectrum of the original signal to be centered around the carrier frequency, ωc.

## Slide 5: Type of Modulation
Pulse Modulation: The original analog signal modulates the following parameters of a digital pulse train:
  Pulse Amplitude Modulation (PAM)
  Pulse Width Modulation (PWM)
  Pulse Position Modulation (PPM)
  Pulse Code Modulation (PCM)
  Delta Modulation (DM)
In pulse modulation the spectrum of the original signal is not shifted. Pulse modulation is a digital pulse coding schemes used to describe the analog signal.

## Slide 6: Double-Sideband Amplitude Modulation
Double-sideband, suppressed-carrier (DSB-SC) modulation

## Slide 7: Demodulation
Demodulator: recovering the message signal at the receiver from the modulated signal.

## Slide 8: Type of Modulators
Multiplier Modulators: A variable gain amplifier in which the gain parameter (such as the  of transistor) is controlled by the message signal m(t) and the input is the carrier signal.
Nonlinear Modulators: Nonlinear devices such as diode or transistors are used to output modulated signal.
]-]
Single balanced modulator because one of the input does not appear at the output z(t)

## Slide 9: Type of Modulators
Switching Modulators: Switching is equivalent to multiplying the message signal m(t) by periodic pulses w(t) with fundamental period Tc.

## Slide 10: Type of Modulators
Switching Modulators

## Slide 11: Circuit of Switching Modulators
Diode-bridge electronic switch:
Shunt-bridge diode modulator
Diode-bridge electronic switch
Series-bridge diode modulator
When Vc > Vd all diodes are open and matched
VD1 = VD2
VD1 = Vc – Va
VD2 = Vc – Vb
Va = Vb

## Slide 12: Circuit of Switching Modulators
Ring Modulator
During Positive cycle of carrier:
- D1 & D3 Conducts
- a connected to c & b connected to d
- output proportional to m(t)
During Negative cycle of carrier:
- D2 & D4 Conducts
- a connected to d & b connected to c
- output proportional to -m(t)
Double Balanced Modulator

## Slide 13: Demodulation of DSB-SC Signals
For demodulation, the receiver must generate a carrier that is synchronous (coherent) in phase and in frequency with incoming carrier.
- The received signal might suffer from some unknown frequency or
phase shift.
- The receiver must be sophisticated to generate a local oscillator
cos[(ωc+Δω)t - θd)] purely from the received signal r(t).
Challenge of coherent demodulation for DSB-SC signals
- Amplitude modulation (AM) that transmit the carrier with the modulated
signal will simplify the job of the receiver.

## Slide 14: Amplitude Modulation (AM)
Transmit the modulated signal with the carrier signal to simplify the complexity of the receivers.
+
for all t
Condition for demodulation using envelope detection
Modulation index

## Slide 15: Example: Tone Modulation
Sketch φAM(t) for modulation indices of µ = 0.5 and µ = 1, when m(t) = b cosωmt.

## Slide 16: Sideband and Carrier Power
carrier
sidebands
Power of the carrier (wasted):
Power of the sidebands:
Power efficiency:

## Slide 17: Example
Determine η and the percentage of the total power carried by the sidebands of the AM wave for tone modulation when
(a) µ =1 (b) µ = 0.5 (c) µ = 0.3

## Slide 18: Demodulation of AM Signals
Rectifier

## Slide 19: Demodulation of AM Signals
Envelope Detector
RC too large
e-t/RC
TC
TB
TC
TB

## Slide 20: Bandwidth-Efficient Amplitude Modulations
Single-Sideband (SSB) modulation, which remove either the LSB or the USB so that for one message signal m(t), there is only a bandwidth of B Hz.
Quadrature Amplitude (QAM) modulation, which utilize spectral redundancy by sending two messages over the same bandwidth, 2B Hz .
The bandwidth of Amplitude Modulation is 2B Hz.
How to reduce bandwidth?

## Slide 21: Amplitude Modulation: Single Sideband (SSB)
Single-Sideband (SSB) modulation, use Hilbert transform to remove the LSB or USB.

## Slide 22: Hilbert Transform
Hilbert Transform
h(t)
H(f)
m(t)
mh(t)
M(f)
Mh(f)
Hilbert transform is an ideal phase shifter that shifts the phase of every positive spectral component by -π/2.

## Slide 23: Time Domain Representation of SSB Signals

## Slide 24: Coherent Demodulation of SSB-SC
These terms can be filtered out by using low-pass filter

## Slide 25: Tone Modulation Example: SSB
Find for the simple case of a tone modulation, that is, a modulating signal that is sinusoid m(t) = cosωmt. Also demonstrate the coherent demodulation of the SSB signal.

## Slide 26: SSB Modulation Systems
Common Methods to Generate SSB
1- Phase Shift
2- Selective-filtering
3- Weaver’s
These modulation methods require that the baseband signal spectrum have little power near the origin, because ideal filters and Hilbert transformer are not realizable.
Speech signal has no DC and little power near the origin. For speech recognition we can eliminate all frequency components below 300 Hz.

## Slide 27: SSB Phase Shift Modulation System

## Slide 28: SSB Selective-Filtering Modulation System
The signal is passed through a sharp cutoff filter to eliminate the undesired sideband. Low-pass filter to eliminate the USB spectrum, and high-pass filter to eliminate the LSB spectrum.
Weaver’s method modulates the signal to a low carrier frequency first and filter out the undesired SSB, after that modulate it again to the desired high carrier frequency.

## Slide 29: Demodulation of SSB Signal with a Carrier
Where E(t) the envelope
of
If A >> |m(t)|, use Power series expansion and discard higher order

## Slide 30: Quadrature Amplitude Modulation (QAM)
It is difficult to generate accurately SSB-SC and requires large power A >>|m(t)|, so QAM offers an attractive alternative.
QAM operates by transmitting two DSB signals via carrier of the same frequency but in phase quadrature.
Transmitter
Receiver

## Slide 31: Quadrature Amplitude Demodulation
In-phase channel
Quadrature channel

## Slide 32: Quadrature Amplitude Modulation (QAM)
Drawback of QAM
An error in the phase or the frequency of the carrier at the demodulator will result in loss and Cochannel interference.
The output of the low-pass filter:
If θ is small then the distortion is tolerable for some applications.

## Slide 33: Amplitude Modulations: Vestigial Sideband (VSB)
VSB signals are relatively easy to generate, and their bandwidth is typically 25% greater than that of SSB signals.

## Slide 34: Demodulation of Vestigial Sideband (VSB)
-----------> 1
Substitute equation 1 and filter out spectra at ± 2 fc
M
| f |  B

## Slide 35: Demodulation of Vestigial Sideband (VSB)
For envelope demodulation, VSB+C require larger carrier than DSB+C but less than SSB+C.
The carrier frequency of a certain VSB signals is fc = 20 kHz, and the baseband signal bandwidth is 6 kHz. The VSB shaping filter Hi(f) at the transmitter is shown below, find the filter H0(f) at the receiver for distortionless reception.

## Slide 36: Use of VSB in Broadcast Television
TV Broadcasting
Bandwidth 4.5 MHz
Has sizable power in the low-frequency region
Envelope detector is used instead of synchronous to reduce the cost of the receiver.
BW for SSB = 4.5 MHz
BW for DSB = 9 MHz
BW for VSB = 6 MHz

## Slide 37: Frequency Division Multiplexing (FDM)
Signal multiplexing allows the transmission of several signals on the same channel.
Time Division Multiplexing (TDM): several signals time-share the same channel.
Frequency Division Multiplexing (FDM): several signals share the band of a channel.
Telephone Analog L-carrier hierarchy
Using SSB+C
48 kHz
240 kHz
2400 kHz
600 voice channel

## Slide 38: Frequency Division Multiplexing (FDM)

## Slide 39: Local Carrier Synchronization
It is difficult for the receiver to generate the carrier in synchronization with the received carrier because of frequency shift due to Doppler effect and phase shift due to traveling.
Doppler Effect
ve is the speed of receiver
Phase Shift
Two ways to recover the incoming carrier at the receiver:
- The transmitter transmits a pilot (sinusoid) signal
- The receiver uses nonlinear device to generate a separate
carrier component to be extracted by narrow bandpass
filters.
d Traveled distance by radio wave

## Slide 40: Phase-Locked Loop and Applications (PLL)
Typically used to track the phase and the frequency of the carrier component of an incoming signal.
Application of PLL
Synchronous demodulation
Timing recovery in digital receiver
Remember frequency or phase shift can be represented as phase shift:

## Slide 41: Phase-Locked Loop and Applications (PLL)
Output of the multiplier
eo(t) depends on the difference between the received phase θi and the generated θo at the receiver. eo(t) will control the oscillation of the voltage controlled oscillator to phase locked with θi.
Output of the loop filter
Instantaneous frequency of VCO =

## Slide 42: Carrier Acquisition in DSB-SC
Signal-Squaring Method
Two methods to generate the carrier at the receiver using PLL.

## Slide 43: Carrier Acquisition in DSB-SC
Costas Method

## Slide 44: NTSC Television Broadcasting System
NTSC: National Television System Committee
The information of the entire picture is transmitted by transmitting an electrical signal proportion to the brightness level of the pixels taken in a certain sequence.
The optical system of the television camera tube generates a focused image on a photo cathode, which eventually produces electrically charged image on another surface (target mosaic).
Charge Coupled Device
Electron gun scans the target mosaic.

## Slide 45: NTSC Television Broadcasting System
NTSC: National Television System Committee
Few pixels
Low Resolution
Less data
More pixels
High Resolution
More data

## Slide 46: NTSC Television Broadcasting System
Scanning Pattern
Line scanning
Frame scanning
Time to scan one horizontal line: 53.5 µs
Time to fly back to scan next line (blank no data): 10 µs
Number of lines per frame 525 line/frame
Time to scan one frame: 15.71 ms
Time to fly back to scan next frame (blank): 0.95 ms
Total number of frames per second: 60 frame/sec

## Slide 47: NTSC Television Broadcasting System
Scanning Pattern
DSB
VSB+C
white: more positive charge

## Slide 48: NTSC Television Standard and Bandwidth
525 lines per frame
495 lines per frame are active scanning
40 frames per second needed to avoid flicker and jerky motion. 30 frames per second to conserve bandwidth in NTSC standard
Frame scanned twice and in each scan only 247.5 line is used.
First scan is the solid lines and the second scan is dashed lines.
Bandwidth
If frame consist of 525 by 525 pixels and 30 frames per second, then
BW = 525 X 525 X 30 = 8.27 X 106 pixels (pulse) per second.
= 4.135 MHz

## Slide 49: Television Transmitter

## Slide 50: Television Receiver
Superheterodyne Receiver

## Slide 51: Compatible Color Television (CCTV)
Luminance
Chrominance

## Slide 52: Color Television Receiver (CCTV)