## Slide 1: Ch 4 Angle Modulations and Demodulations
ENGR 4323/5323
Digital and Analog Communication
School of Engineering
University of Central Oklahoma
Dr. Mohamed Bingabr

## Slide 2: Chapter Outline
Nonlinear Modulation
Bandwidth of Angle Modulation
Generating of FM Waves
Demodulation of FM Signals
Effects of Nonlinear Distortion and Interference
Superheterodyne Analog AM/FM Receivers
FM Broadcasting System

## Slide 3: Baseband Vs. Carrier Communications
Angle Modulation: The generalized angle θ(t) of a sinusoidal signal is varied in proportion to the message signal m(t).
Two types of Angle Modulation
Frequency Modulation: The frequency of the carrier signal is varied in proportion to the message signal.
Phase Modulation: The phase of the carrier signal is varied in proportion to the message signal.
Instantaneous Frequency

## Slide 4: Frequency and Phase Modulation
Phase Modulation:
Power of an Angle-Modulated wave is constant and equal A2/2.
Frequency Modulation:

## Slide 5: Example of FM and PM Modulation
Sketch FM and PM waves for the modulating signal m(t). The constants kf and kp are 2π x105 and 10π, respectively, and the carrier frequency fc is 100 MHz.
99.9 MHz < fi < 100.1 MHz

## Slide 6: Example of FM and PM Modulation
Sketch FM and PM waves for the digital modulating signal m(t). The constants kf and kp are 2π x105 and π/2, respectively, and the carrier frequency fc is 100 MHz.
Frequency Shift Keying (FSK)
Phase Shift Keying (PSK)
Note: for discontinuous signal kp should be small to restrict the phase change kpm(t) to the range (-π,π).

## Slide 7: PSK & FSK in Digital Communication

## Slide 8: Bandwidth of Angle Modulated Waves
where
The bandwidth of a(t), a2(t), an(t) are B, 2B, and nB Hz, respectively. From the above equation it seems the bandwidth of angle modulation is infinite but for practical reason most of the power reside near B Hz since higher terms have small power because of n!.
Expand
using power series expansion

## Slide 9: Narrowband PM and FM
When kf a(t) << 1
The above signal is Narrowband FM and its bandwidth is 2B Hz.
Same steps can be carried out to find the Narrowband PM.
Note: the above equation is similar to amplitude modulation but the waveform are different.

## Slide 10
m(t)
fc = 300 FM modulation kf = 120  kf a(t) = 6 NBFM (kf a(t)max <<1)
fc = 300 PM modulation kp = 10  kp mp = 31.4 NBPM (kpm(t)max << 1)

## Slide 11
fc = 300 FM modulation kf = 10  kf a(t) = 0.5 NBFM (kf a(t)max <<1)
fc = 300 PM modulation kp = 0.1  kp mp = 0.314 NBPM (kpm(t)max << 1)
m(t)

## Slide 12
ts=1.e-4; kf = 10*pi; kp = 0.1*pi;
fc = 300; t=-0.05:ts:0.05; Ta = 0.02;
triangle = @(z)(1-abs(z)).*(z>=-1).*(z<1);
m_sig = 1*(triangle((t+0.01)/Ta) - triangle((t-0.01)/Ta));
m_intg = ts*cumsum(m_sig);
s_fm = cos(2*pi*fc*t + kf*m_intg);
s_pm = cos(2*pi*fc*t + kp*m_sig);
subplot(311);
plot(t, m_sig)
subplot(312);
plot(t, s_fm)
subplot(313);
plot(t, s_pm)
s_nbfm = cos(2*pi*fc*t) - kf*m_intg.*sin(2*pi*fc*t);
s_nbpm = cos(2*pi*fc*t) - kp*m_sig.*sin(2*pi*fc*t);
figure;
subplot(311);
plot(t, m_sig)
subplot(312);
plot(t,s_nbfm)
subplot(313);
plot(t, s_nbpm)
figure; plot(t, m_intg)
Code to demonstrate the effect of the condition for
NBFM (kf a(t)max <<1) and
NBPM (kpm(t)max << 1)

## Slide 13: Wideband FM (WBFM)
In many application FM signal is meaningful only if its frequency deviation is large enough, so kf a(t) << 1 is not satisfied, and narrowband analysis is not valid.
Fourier Transform
Hz
+
Hz

## Slide 14: Wideband FM (WBFM)
Hz
is the deviation ratio
Where
When Δf >> B the modulation is WBFM and the bandwidth is BFM = 2 Δf
When Δf << B the modulation is NBFM and the bandwidth is BFM = 2B
A better estimate: Carson’s rule
Peak frequency deviation in hertz

## Slide 15: Wideband PM (WBPM)
The instantaneous frequency
Deviation ratio
Peak frequency deviation in hertz

## Slide 16: Example
Estimate BWFM and BWPM for the modulating signal m(t) for kf =2π x105 and kp = 5π. Assume the essential bandwidth of the periodic m(t) as the frequency of its third harmonic.
Repeat the problem if the amplitude of m(t) is doubled.
Repeat the problem if the time expanded by a factor of 2: that is, if the period of m(t) is 0.4 msec.
BFM = 230 BPM = 130 kHz
BFM = 430 BPM = 230 kHz
BFM = 215 BPM = 65 kHz

## Slide 17: Example
An angle-modulated signal with carrier frequency ωc = 2 105 is described by the equation
Find the power of the modulated signal.
Find the frequency deviation Δf.
Find the deviation ratio .
Find the phase deviation Δø.
Estimate the bandwidth of .
Read the Historical Note: Edwin H. Armstrong (page 242)
P = 50
Δf = 12,387 Hz
 = 12.387
Δø = 15 rad
B = 26,775 Hz

## Slide 18: Generating FM Waves
Two Methods:
Direct method
Indirect method using NBFM Generation
The Direct Method
The frequency of a voltage-controlled oscillator (VCO) is controlled by the voltage m(t).
Use an operational amplifier to build an oscillator with variable resonance frequency ωo. The resonance frequency can be varied by variable capacitor or inductor. The variable capacitor is controlled by m(t).

## Slide 19: The NBFM Generation
With the NBFM generation, the amplitude of the NBFM modulator will have some amplitude variation due to approximation.

## Slide 20: Distortion with NBFM Generation
Example 5.6: Discuss the nature of distortion inherent in the Armstrong indirect FM generator.
Amplitude and frequency distortions.
kf a(t) << 1

## Slide 21: Distortion Removal on NBFM Generation
Bandpass Limiter

## Slide 22: Indirect Method of Armstrong
NBFM is generated first and then converted to WBFM by using additional frequency multipliers.
Example of frequency multiplier is a nonlinear device
Devices of higher multiplier

## Slide 23: Indirect Method of Armstrong
For NBFM  << 1.
For speech fmin = 50Hz, so if Δf = 25 then   25/50 = 0.5,

## Slide 24: Example
Design an Armstrong indirect FM modulator to generate an FM signal with carrier frequency 97.3 MHz and Δf = 10.24 kHz. A NBFM generator of fc1 = 20 kHz and Δf = 5 Hz is available. Only frequency doublers can be used as multipliers. Additionally, a local oscillator (LO) with adjustable frequency between 400 and 500 kHz is readily available for frequency mixing.
M1 = 24 M2 = 27 fLO = 440 kHz

## Slide 25: Demodulation of FM Signals
A frequency-selective network with a transfer function of the form |H(f)|=a2f + b over the FM band would yield an output proportional to the instantaneous frequency.
Differentiator
|H(f)|

## Slide 26: Demodulation of FM Signals

## Slide 27: Practical Frequency Demodulators
if
The slope is linear over small band, so distortion occurs if the signal band is larger than the linear band.
Zero-crossing detectors: First step is to use amplitude limiter and then the zero-crossing detector.
Instantaneous frequency = the rate of zero crossing

## Slide 28: FM Broadcasting Standard
Federal Communications Commission (FCC) specifications for FM communication
Frequency range = 88 to 108 MHz
Channel separations = 200 kHz,
Peak frequency deviation = 75 kHz
Transmitted signal should be received by monophonic and stereophonic receivers.
90
88
108 MHz
90.2
200 KHz
75 KHz
150 KHz
89.8
Filter
10.7
MHz

## Slide 29: Superheterodyne Analog AM/FM Receivers
fIF = 455KHz (AM radio);
10.7 MHz (FM);
38 MHz (TV)
AM stations that are 2 fIF apart are called image stations and both would appear simultaneously at the IF output.
RF filter eliminates undesired image station, while IF filter eliminates undesired neighboring stations.
90 desired signal
90.2 adjacent
111.4 image
90+10.7=100.7
fc = 10.7
10.7 , 190.7
10.5 , 190.9
90
90.2
111.4
10.7, 212.1
10.7

## Slide 30
Homework Problem 5.4-2

## Slide 31
Homework Problem 5.6-2

## Slide 32: Effect of Nonlinear Distortion and Interference
Immunity of Angle Modulation to Nonlinearities
Vulnerability of Amplitude Modulation to Nonlinearities

## Slide 33: Interference Effect
Angle Modulation is less vulnerable than AM to small-signal interference from adjacent channels.
for I << A
The output of ideal phase and frequency demodulators are
For PM
For FM
Interference is inversely proportional to the carrier amplitude (capture effect).

## Slide 34: Preemphasis and Deemphasis in FM
For audio signal the PSD is concentrated at low frequency below 2.1 kHz, so interference at high frequency will greatly deteriorate the quality of audio signal.
Preemphasis
Filter
Deemphasis
Filter
Noise
With white noise, the amplitude interference is constant for PM but increase with ω for FM.

## Slide 35: Preemphasis and Deemphasis (PDE) in FM
Preemphasis Filter
Deemphasis Filter
2.1 kHz
30 kHz

## Slide 36: Preemphasis and Deemphasis (PDE) in FM
For 2f << ω1
For ω1 << 2f << ω2
Where K is the gain and = ω2 / ω1
PDE is used in many applications such as recording of audiotape and photograph recording, where PDE depends on the band.

## Slide 37: FM Broadcasting System (Transmitter)
Monophonic and Stereophonic Broadcasting System

## Slide 38: FM Broadcasting System (Receiver)