## Slide 1: Sampling: The Bridge from Continuous to Discrete
Chapter 3
Dr. Mohamed Bingabr
University of Central Oklahoma
ENGR 4333/5333: Digital Signal Processing

## Slide 2: Outline
Sampling Theorem
Signal Reconstruction
Practical Difficulty in Sampling and Reconstruction
Sampling of Bandpass Signals
Spectral Sampling Theorem
Analog to Digital Conversion
Digital to Analog Conversion

## Slide 3: 3.1 & 3.2 Sampling and Signal Reconstruction

## Slide 4: Sampling Theorem
A real signal whose spectrum is bandlimited to B Hz [X( f ) = 0 for | f | >B ] can be reconstructed exactly from its samples taken uniformly at a rate Fs > 2B samples per second. When Fs = 2B then Fs is the Nyquist rate.

## Slide 5: Ideal Signal Reconstruction from Samples
In Frequency Domain
In Time Domain

## Slide 6: Review of Pulse Train
ωs
2ωs
-ωs
-2ωs
Xk
FT
Pk
Ideal sampling impulses
Practical sampling pulses

## Slide 7: Practical Sampling
In practice we sample the signal x(t) by multiplying it by a T-periodic train

## Slide 8: Example of Practical Sampling

## Slide 9: Matlab Example for Signal Reconstruction
x = @(t) cos(pi*t/2);
t = linspace(-2,2,501);
xhatN = 0; T = 1;
for n = -2:2,
xhatN = xhatN + x(n*T)*sinc((t-n*T)/T);
End
plot(t,xhatN);
dt = t(2)-t(1); RMSerror = sqrt(sum((xhatN-x(t)).^2)*dt)
Ans: RMSerror = 0.0030

## Slide 10: Practical Interpolation
The Zero-Order Hold Filter

## Slide 11: 3.3 Practical Difficulties in Sampling

## Slide 12: Practical Difficulty in Sampling and Reconstruction
Aliasing: If a continuous time signal is sampled below the Nyquist rate then some of the high frequencies will appear as low frequencies and the original signal can not be recovered from the samples.
For the spectra of real signals, the tail appears to fold or invert about Fs/2. Thus, a component of frequency Fs/2 + f1 shows up as or impersonates a component of lower frequency Fs/2−f1 in the reconstructed signal. This causes distortion of low-frequency (|f| < Fs/2) signal content. The frequency Fs/2 is called the folding frequency, and the tail inversion is known as spectral folding or aliasing.
If a signal is time limited, it cannot be bandlimited, and vice versa.

## Slide 13: Aliasing in Sinusoids
A sinusoid with 11 Hz frequency sampled with sampling rate Fs = 10 z.
11
-11
21
-1
1
-21
LPF with BW = 5
11
-11

## Slide 14: Practical Difficulty in Sampling and Reconstruction
Anti-Aliasing Filter

## Slide 15: Multiple Aliasing
The apparent frequency fa that is in the fundamental band (−Fs/2 ≤ fa ≤ Fs/2) of undersampled signal of frequency f0 is.
where is the modulo operation a modulo b.
Example:
What are the apparent frequencies of sinusoidals with 3, 8, 23 Hz frequency sampled with sampling rate Fs = 10 z.

## Slide 16: 3.4 Sampling of Bandpass Signals

## Slide 17: Sampling of Bandpass Signals
Sampling a bandwidth B bandpass signal:
original spectrum,
f2 = 4B and Fs = 2B,
f2 = 4B and Fs = 4.75B,
f2 = 4B and Fs = 3.25B,
general sampling case
B=1k
K = 0, 1, 2, . . .

## Slide 18
B
Sampling a bandwidth B bandpass signal:
original spectrum,
f2 = 4B and Fs = 2B,
f2 = 4B and Fs = 4.5B,
f2 = 4B and Fs = 3.5B,
f2
f1
B = f2 – f2
2f1
2f2
Fs =2B
Fs
Example 3.6: Determine the permissible range of the uniform sampling rate for a bandpass signal with f1 = 25 kHz and f2 = 35 kHz.

## Slide 19: 3.5 Spectral Sampling Theorem Skip section 3.5: will be covered in DFT

## Slide 20: The Spectral Sampling Theorem
The spectral sampling theorem states that the spectrum X(ω) of a signal x(t) timelimited to a
duration of To seconds can be reconstructed from the samples of X(ω) taken at a rate R samples/Hz, where R  To (the signal width or duration) is in seconds. The frequency resolution fo = 1/ To.

## Slide 21: Reconstructing x(t) from Spectral Samples
If the pulse x(t) is centered at the origin, then Tc = 0
Example 3.7: Find the unit duration signal x(t), centered at the origin, whose spectrum X(ω), when sampled at intervals of fo = 1 Hz (the Nyquist rate), is X(k2fo) = 1 for k = 0 and zero otherwise.

## Slide 22: 3.6 Analog to Digital Conversion

## Slide 23: 3.6 Analog to Digital Conversion (ADC)
01110011 11001101 01011100
ADC

## Slide 24: 3.6 Analog to Digital Conversion
Analog signal: Its amplitude can take on any value over a continuous range.
Digital signal: Its amplitude can take on only a finite number of values.
Sampling and Linear Quantization

## Slide 25: 3.6 Analog to Digital Conversion
How many bits per sample?
 = 2 Vref / L
 : Quantization level
L : Number of levels between -Vref and Vref
B : Number of bits for each sample
Quantization error Qe = /2
Linear Quantization
 = Vref /
Qe = Vref /

## Slide 26: 3.6 Analog to Digital Conversion
Pulse Code Modulation (PCM)
Data Transmission = 3 Fs bits/sec

## Slide 27: Digitizing Voice and Audio
Telephone Communication:
Sampling Rate fs = 8000 samples/sec
Number of bits = 7 bits/sample
Data transmission = 8000*7 = 56000 bits/sec (56 kbps)
Music:
Sampling Rate fs = 44100 samples/sec
Number of bits = 16 bits/sample
Data transmission = 44100*16 = 1.4 million bits/sec (1.4 Mbps)
Example
A signal x(t) bandlimited to 3 kHz is sampled at a rate % higher than the Nyquist rate. The maximum acceptable error in the sample amplitude (the maximum error due to quantization) is 0.5% of the peak amplitude Vref . The quantized samples are binary coded. Find the required sampling rate, the number of bits required to encode each sample, and the bit rate of the resulting PCM signal.

## Slide 28
Rounding Asymmetric
Asymmetric Quantization Converter
Zero is included and levels above zero does not equals levels below zero.
Find xq for x =7.74 and B = 3bits. Vref = 10
Truncating Asymmetric

## Slide 29
Find xq for x =7.74 and B = 3bits. Vref = 10
Symmetric Quantization Converter
Truncating Symmetric
Rounding Symmetric
Zero is not included and levels above zero equals levels below zero.

## Slide 30
clear all
[sig Fs]=audioread('Song.wav');
Vref = max(abs(sig));
B = 2; Delta = 2*Vref/(2^(B-1));
xqra = Delta*floor(sig/Delta+1/2);
xqra(xqra>Vref-Delta) = Vref-Delta; xqra(xqra<-Vref) = -Vref;
sound(xqra, Fs)
8 Bits
# Levels = 256
2 Bits
# Levels = 4
Rounding Asymmetric

## Slide 31: Example
Drill 3.14: Consider the common situation where a signal x(t) becomes 0 for an extended period of time. Explain why an asymmetric rounding converter is better than symmetric rounding converter in the case where low-level noise corrupts x(t). Which asymmetric converter is best, rounding or truncating? Explain.

## Slide 32
Coding Method for asymmetric
Two’s Complement
Offset Binary
Example 3.9: Assuming a 4-bit asymmetric converter is used, determine the value xq that corresponds to the two’s complement code word 1101. What is the value if the code word is offset binary? How do the values change if the converter is instead a symmetric converter?
c0
c1
c2
Note: for symmetric add /2 to xq
Example of Two’s Complement
3  011
To find the binary for a negative value then reverse the bits of the positive value and add 1.
-3  100 + 001 = 101

## Slide 33
Example 3.10: Consider the signal x(t) = cos(2πt/25). Using sampling interval T = 1 s, reference Vref = 1, and B = 2 bits, plot the quantized signal xq[n] over one period of x(t) using rounding asymmetric quantization methods of Eq. (3.23).
Matlab Code
T = 1; Vref = 1; B = 2; Delta = 2*Vref/(2^B);
x = @(t) cos(2*pi*t/25); n = (0:25);
xqra = Delta*floor(x(n*T)/Delta +1/2);
xqra(xqra>Vref-Delta) = Vref-Delta; xqra(xqra<-Vref) = -Vref;
stem(n,xqra);
Rounding asymmetric
Truncating asymmetric
Rounding symmetric
Truncating symmetric

## Slide 34: Nonlinear Quantization
Reduce quantization error for smaller signal amplitudes at the expense of larger signal amplitudes.
In telephone the bit rate for linear quantization is twice that for nonlinear to establish the same sound quality.
Linear quantization
Nonlinear quantization

## Slide 35: Nonlinear Quantization
-law Compression
The compression parameter μ determines the level of compression. Large μ increases resolution for small signal amplitudes, all at the price of more coarseness for large amplitudes.
Vref = 10 µ = 100
x1 = 1 x1 = 5.196
x2 = 8 x2 = 9.52
Inverse -law Compression
Example

## Slide 36: Analog-to-Digital Converter Implementation
Counting Converter

## Slide 37: 3.7 Digital to Analog Conversion

## Slide 38: Digital-to-Analog Conversion

## Slide 39: Source of Distortion in Signal Reconstruction
1- Aperture Effect: Distortion from the Zero-Order- Hold
Hzoh()
H()
Hlpf()
=

## Slide 40: Source of Distortion in Signal Reconstruction
2- Distortion from Linear Quantization
Quantization error eq value is in the range (-/2, /2)
Energy (or power) of the quantization error is the means square quantization error Eq
From probability the eq is a random variable with uniform density function

## Slide 41: Example 3.11
A periodic sinusoidal signal x(t) of amplitude 12 volts is quantized and binary coded. Assuming the power of the signal-to-quantization noise ratio must exceed 20000, determine the smallest number of bits B needed to encode each sample.
Answer: B  6.8514 so choose B = 7