## Slide 1: Discrete Fourier Transform
Chapter 9
Dr. Mohamed Bingabr
University of Central Oklahoma
ENGR 4333: Digital Signal Processing

## Slide 2: Outline
The Discrete Fourier Transform
Discrete-Time Filtering Using the DFT

## Slide 3
CTFT
DFT
=
DTFT

## Slide 4: The Discrete Fourier Transform
The direct and inverse relationships between a length-N signal x[n] and the N samples of the spectrum X[k] deﬁne the discrete Fourier transform (DFT). The DFT proves extremely useful in numerical computations of the discrete time Fourier transform and its inverse (DTFT).
DFT
Frequency resolution
X[k] = X*[N - k] where k =1, 2, … , (N-1)/2 for odd N or (N-2)/2 for even N.

## Slide 5: Example
Find the DFT of the length-3 signal x[n] = 3δ[n] + 2δ[n−1] + 3δ[n−2]. Compare the DFT spectrum X[k] with the corresponding DTFT spectrum X(Ω).
Solution
k = 0, 1, 2

## Slide 6: The Discrete Fourier Transform with Zero Padding
The DFT yields samples of the DTFT spaced at frequency intervals of Ω0 =2π/N. In this way, the DFT size N determines the frequency resolution Ω0. To see more frequency components of DTFT we improve the frequency resolution by increasing N (number of samples in the signal x[n]). Since the number of samples already determined based on the sampling theorem, we can increase N by padding x[n] with zeros.
Zero padding allows us to obtain more samples of X(Ω) for clarity. Furthermore, this process does not change the underlying signal x[n], which means that zero padding does not aﬀect the underlying spectrum X(Ω).
Example: a signal x(t) = sin(2πt) + sin(2π1.5t) + sin(2π3t) sampled at the Nyquist rate fs = 6 samples/second. The signal is sampled for 1 second. What are the DFT components X[k]? Will you be able to see the 1.5 Hz sinusoidal signal?

## Slide 7: Example
Using zero padding, ﬁnd the 6-point DFT of the length-3 signal x[n] = 3δ[n] + 2δ[n−1] + 3 δ[n−2]. Compare the 6-point DFT X[k] with the corresponding DTFT spectrum X(Ω).
Solution

## Slide 8: Matrix Representation of the DFT and Its Inverse
For large N it is cumbersome to manually evaluate the DFT and its inverse. Fortunately, both represent sets of N linear equations in N unknowns. Consequently, both can be expressed in matrix form, suitable for simple computer evaluation.

## Slide 9: Example (read in textbook)
Use MATLAB to compute and plot the DFT of the length-3 signal x[n] = 3δ[n] + 2δ[n−1] + 3 δ[n−2]. Determine the zero padding needed to achieve a DFT frequency resolution of Ω0 = π/10. Compare the DFT spectrum X[k] with the corresponding DTFT spectrum X(Ω).
Solution
N = 20; Omega0 = 2*pi/N; k = (0:N-1); n = (0:N-1);
x = [3;2;3;zeros(N-3,1)];
DN = exp(-1j*Omega0*k'*n); X = DN*x;
Omega = linspace(0,2*pi,6001); XOmega = exp(-1j*Omega).*(2+6*cos(Omega));
subplot(121); stem(k*Omega0,abs(X)); line(Omega,abs(XOmega));
subplot(122); stem(k*Omega0,angle(X)); line(Omega,angle(XOmega));

## Slide 10: DFT Interpolation to Obtain the DTFT
We can determine the entire X(Ω) from the samples of the DFT using interpolation. This is similar to finding x(t) from x[n] samples by interpolation.
The inner sum on the right-hand side is a geometric progression and can be simplified as follow in the next slide.

## Slide 11: DFT Interpolation to Obtain the DTFT
N = 12
k = 0
k = 1
Ω0 = 2π/N = π/6
k = 2
k = 6
π
π/6
π/3
Ω0 = 2π/N

## Slide 12: Example (read it textbook)
Using interpolation, determine the DTFT X(Ω) if the DFT of the corresponding 3-point x[n] is given by X[0] = 8, X[1] = ejπ/3, and X[2] = e−jπ/3.
Solution

## Slide 13: DTFT  DFT
DTFT
IDTFT
IDFT
DFT
Frequency
Sampling
Time Sampling
Frequency
Interpolation
Time
Interpolation
FT
IFT
Time Sampling

## Slide 14: Confining x[n] to 0  n ≤ N-1for Unique DFT
The summation in the DFT definition starts from n = 0 to N-1, so how do we find the DFT for a signal that starts at n = 9?
The DFT for the signals xa[n], xb[n], and xc[n], are the same.
Can we just shift it to start at zero? NO
So, how do we confine x[n] to 0  n ≤ N-1 ?

## Slide 15: How to Confine x[n] to 0  n ≤ N-1for Unique DFT
The DFT for the signals w[n] and x[n] of size N = 6 are the same.
The inverse DFT will produce a periodic x[n] signal.
n = 9 to 14
n = 0 to 5

## Slide 16: Confining x[n] to 0  n ≤ N-1 for Unique DFT
Modulo-N Shift
Modulo-N is used in DFT to shift an arbitrary N-point sequence into the range 0 to N-1.
The N uniform samples of the DTFT of a length-N sequence remain unchanged under the modulo-N shift of the sequence.
Modulo-N value of a positive n is the remainder of the division of n by N.
Modulo-N value of a negative n is N minus the remainder of the division of |n| by N.
If DFT requires the confinement of the signal x[n] between 0 and N-1 then how do we perform time shifting, reversal, and convolution for signal processing?

## Slide 17: Modulo-N Shift of x[-n]
The Modulo-N Reflection
Just as with a linear representation, the circular representation of time reversal is just a reflection about the vertical axis.
Time Reversal Property

## Slide 18: Modulo-N Shift of x[n-m]
The Circular Shift Modulo-N Reflection x[n − mN]
A linear shift of x[n] by m samples yields the signal x[n − m], which is a length-N signal with a range m ≤ n ≤ m + N − 1.
As with the case of reflection, we instead seek a form that will retain the range 0 ≤ n ≤ N − 1.
A modulo-N shift of x[n − m], also called a circular shift, accomplishes exactly this task.
Circular Shifting Property
N = 6

## Slide 19: Circular Convolution
The two sequences to be convolved must have the same length. If not, we should append enough zeros to the smaller sequence to ensure equal lengths of both sequences.
y[0]
y[1]
y[2]
y[3]
Y(k) = X [k] H [k]

## Slide 20: Signal Processing and Filtering Using the DFT
Find the output y[n] of the system described by the impulse response
h[n] = δ[n] + δ[n−1] + δ[n−2] and with input x[n] = δ[n−1] + 2δ[n−2] + 3δ[n−3]+ 4δ[n−4]
h[n]
H(z)
H(Ω)
H[k]
x[n]
y[n] = x[n] * h[n]
Y(z) = X(z) H(z)
Y(Ω) = X(Ω) H(Ω)
Y [k] = X [k] H [k]
Size of y[n]: Ny = Nx + Nh -1
What is the size of y[n]?
Will the inverse DFT of Y[k] give us y[n]?

## Slide 21: Circular and Linear Convolution
Circular Convolution is different from linear convolution. In Circular all N samples of x[n] and h[n] are aligned and multiplied for any value of n.
For linear system analysis we need to modify circular convolution to be similar to linear convolution.
The length N of the signal y[n] which is the result of convolving x[n] with h[n] is N = Nx + Nh -1.
If linear and circular convolutions are to yield identical results, then a necessary condition is that the length of each signal x[n] and h[n] must be extended to N = Nx+ Nh− 1. In other words, we must pad Nh - 1 zeros to x[n] and pad Nx - 1 zeros to h[n].

## Slide 22: Discrete-Time Filtering Using the DFT
The DFT is useful in the computation of direct and inverse Fourier transforms, filtering, convolution, correlation, and others. It can perform these tasks not only for discrete-time systems but also for continuous-time signals and systems. The efficient FFT algorithm, makes the DFT even more appealing.
The DFT-based procedure to find the linear convolution of two signals x[n] and h[n], whose
lengths are Nx and Nh, respectively, is summarized in four steps as follows:
1. Pad Nh − 1 zeros to x[n] to form xpad[n], and pad Nx − 1 zeros to h[n] to form hpad[n].
2. Find Xpad[k] and Hpad[k], the DFTs of xpad[n] and hpad[n].
3. Multiply Xpad[k] by Hpad[k] to obtain Y[k].
4. The desired convolution y[n] is the IDFT of Y[k].
Example: Nx = 7 Nh = 3

## Slide 23: Example
Using DFT-based convolution, determine the output y[n] of an LTID filter with impulse response h[n] = 2δ[n] + 2δ[n − 1] to an input x[n] = 3δ[n] + 2δ[n − 1] + 3δ[n − 2].
After padding h[n] and x[n] with zeros, N = 4 and Ω0 = π/2.
xpad[n] = [3, 2, 3, 0] hpad[n] = [2, 2, 0, 0]
Solution
0 ≤ k ≤ 3
0 ≤ k ≤ 3
[ 8 –j2 4 j2]
[ 4 2–j2 0 2+j2]
[ 32 -4 – j4 0 -4 + j4]

## Slide 24: Continue Example
For small signal convolution might be easier than DFT, but for large signal DFT is faster
Solution
x = [3;2;3]; h = [2;2]; Nx = length(x); Nh = length(h);
xpad = [x;zeros(Nh-1,1)]; hpad = [h;zeros(Nx-1,1)];
N = Nx+Nh-1; n = (0:N-1); k=(0:N-1); Omega0 = 2*pi/N; DN = exp(-1j*Omega0*k’*n);
Xpad = DN*xpad; Hpad = DN*hpad; y = conj(DN)/N*(Xpad.*Hpad)
Ans y = 6 10 10 6

## Slide 26: Block Convolution
In real application the input signal is acquired in real time so its length is not known and it may be very large. This will cause delay and excessive use of memory and processing time. Block convolution is the solution. It break the coming input signal into blocks of determined length N and convolve each block with h[n] and then add the results of all the convolutions.
There are two methods for block convolution:
1- Overlap-and-Add
2- Overlap-and-Save

## Slide 27: Overlap-and-Add Method
In practice the length of the filter impulse response h[n], Nh, is usually smaller than the length of the input blocks Nx. For circular convolution we pad Nh-1 zeros at the end of each data block.

## Slide 28: Example
Using the overlap-and-add method with an Nx = 3 input block size, find the response y[n] of an
LTID system with the Nh = 2 finite impulse response h[n] and input x[n] shown in Figure below.
Solution

## Slide 29: Continue Example

## Slide 30: Continue Example (Matlab Code)
Nx = 3; Nh = 2; N = Nx+Nh-1; Omega0 = 2*pi/N; k = (0:N-1); n = (0:N-1);
DN = exp(-1j*Omega0*k’*n); x0pad = [3;2;3;zeros(Nh-1,1)]; hpad = [2;2;zeros(Nx-1,1)];
X0pad = DN*x0pad; Hpad = DN*hpad; y0 = conj(DN)/N*(X0pad.*Hpad)
Ans y0 = 6 10 10 6
x1pad = [1;0;1;zeros(Nh-1,1)]; X1pad = DN*x1pad; y1 = conj(DN)/N*(X1pad.*Hpad)
Ans y1 = 2 2 2 2
x2pad = [0;1;1;zeros(Nh-1,1)]; X2pad = DN*x2pad; y2 = conj(DN)/N*(X2pad.*Hpad)
Ans y2 = 0 2 4 2

## Slide 31: Overlap-and-Save Method
3- The first block is augmented with Nh-1 zeros.
4- Padd h[n] with Nx-1 zeros to make a length-Nx + Nh-1 signal hpad[n].
1- Section input signal into blocks of length Nx .
2- Augment (padded) the beginning of each block with Nh-1 data points from the end of the previous block.

## Slide 32: Example
Using the overlap-and-save method with an Nx = 3 input block size, find the response y[n] of an LTID system with the Nh = 2 finite impulse response h[n] and input x[n] shown in Figure below.
Solution

## Slide 33: Continue Example
Nx = 4; Nh = 2; N = Nx; Omega0 = 2*pi/N; k = (0:N-1); n = (0:N-1);
DN = exp(-1j*Omega0*k’*n); x0 = [zeros(Nh-1,1);3;2;3]; hpad = [2;2;zeros(Nx-Nh,1)];
X0 = DN*x0; Hpad = DN*hpad; y0 = conj(DN)/N*(X0.*Hpad)
Ans: y0 = 6 6 10 10
x1 = [x0(end-(Nh-1)+1:end);1;0;1]; X1 = DN*x1; y1 = conj(DN)/N*(X1.*Hpad)
Ans: y1 = 8 8 2 2
x2 = [x1(end-(Nh-1)+1:end);0;1;1]; X2 = DN*x2; y2 = conj(DN)/N*(X2.*Hpad)
Ans: y2 = 4 2 2 4

## Slide 34: The Fast Fourier Transform (FFT)
FFT is a computational algorithm developed by in 1965 by Tukey and Cooley to reduce the complexity of calculating the DFT from O(N2) to O(N log2 N). The computational saving are substantial for large N. The FFT algorithm is largely what has made the Fourier transform accessible for digital signal processing.
DFT of size N= 1024 requires on order of approximately one million operation and FFT reduce it to on order of approximately 10 thousand operation. A reduction of 100 fold. The values obtained by the FFT are identical to those obtained by the DFT.
There are many variation of the FFT algorithm but the two main variation are:
1- Decimation in Time (DIT)
2- Decimation in Frequency (DIF)

## Slide 35: Decimation-in-Time Algorithm of FFT
The DFT of N points:
X[0] = x[0] + x[1]
X[1] = x[0] + x[1]
0≤ k ≤ N-1;
Ω0 = 2π/N ;
The DFT of 2 points:

## Slide 36: Decimation-in-Time Algorithm of FFT