## Slide 1: Chapter 25
Current, Resistance, and Electromotive Force

## Slide 2: Goals for Chapter 25
  To understand current and how charges move in a conductor
  To understand resistivity and conductivity
  To calculate the resistance of a conductor
  To learn how an emf causes current in a circuit
  To calculate energy and power in circuits

## Slide 3: Introduction
  Electric currents flow through light bulbs.
  Electric circuits contain charges in motion.
  Circuits are at the heart of modern devices such as computers, televisions, and industrial power systems.

## Slide 4: Current
  A current is any motion of charge from one region to another. Current is the net charge flowing through a cross-sectional area A per unit time.
  An electric field in a conductor causes charges to flow.

## Slide 5: Direction of current flow
  A current can be produced by positive or negative charge flow.
  Conventional current is treated as a flow of positive charges.
  The moving charges in metals are electrons (see figure below).

## Slide 6: Current, drift velocity, and current density
  Current Density

## Slide 7: Resistivity
  The resistivity of a material is the ratio of the electric field in the material to the current density it causes:  = E/J.
  The conductivity is the reciprocal of the resistivity.
  Table 25.1 shows the resistivity of various types of materials.

## Slide 8: Resistivity and temperature
  Resistivity depends on temperature. See Figure 25.6 at the left.
  : Temperature Coefficients of Resistivity

## Slide 9: Resistance
  The resistance of a conductor is R = L/A .
  The potential across a conductor is V = IR.
  If V is directly proportional to I (that is, if R is constant), the equation V = IR is called Ohm’s law.

## Slide 10: Resistors are color-coded for easy identification
This resistor has a resistance of 5.7 kΩ with a tolerance of ±10%.

## Slide 11: Ohmic and nonohmic resistors
Only the resistor in Figure 25.10(a) below obeys Ohm’s law.
Follow Example 25.2.
Follow Example 25.3.

## Slide 12: Ohmic and nonohmic resistors
Example 25.2 and 25.3.
18-gauge copper wire has a cross-sectional area of 8.2x10-7 m2. It carries a current of 1.67 A. Find (a) the electric-field magnitude in the wire; (b) the potential difference between two points in the wire 50 m apart; (c) the resistance of a 50 m length of this wire.
Suppose the resistance of a copper wire is 1.05 Ω at 20o C. Find the resistance at 0oC and 100oC.

## Slide 13: Electromotive force and circuits
  An electromotive force (emf) makes current flow. In spite of the name, an emf is not a force.
  The figures below show a source of emf in an open circuit (left) and in a complete circuit (right).

## Slide 14: Internal resistance
  Real sources of emf actually contain some internal resistance r.
  The terminal voltage of an emf source is Vab =  – Ir.
  The terminal voltage of the 12-V battery shown at the right is less than 12 V when it is connected to the light bulb.

## Slide 15: Symbols for circuit diagrams
  Table 25.4 shows the usual symbols used in circuit diagrams.

## Slide 16: Source in a complete circuit
  What are the voltmeter and ammeter readings Vab and I?

## Slide 17: Using voltmeters and ammeters
  What are the voltmeter and ammeter readings in circuits a and b?

## Slide 18: Potential changes around a circuit
  The net change in potential must be zero for a round trip in a circuit.
  Follow Figure 25.20 at the right.

## Slide 19: Energy and power in electric circuits
If Vab > 0 then the circuit is gaining potential energy qVab.
If Vab < 0 then the circuit is losing potential energy qVab (source).

## Slide 20: Energy and power in electric circuits
  The rate at which energy is delivered to (or extracted from) a circuit element is P = VabI.
  Unit of power: 1 Joule /second = 1 Watt
  The power delivered to a pure resistor is P = I2R = Vab2/R.

## Slide 21: Power input and output
  Find the rates of energy conversion (chemical to electric) and energy dissipation in the battery, the rate of energy dissipation in the 4-Ω resistor, and the battery’s net power output.
  Repeat the above if the resistor value change to 8 Ω .

## Slide 22: Power in a short circuit
  Follow Example 25.10, using Figure 25.25 below.

## Slide 23: Theory of metallic conduction
  Follow the discussion in the text using Figures 25.26 (right) and 25.27 (below). Both illustrate the random motion of electrons in a conductor.
  Follow Example 25.11.

## Slide 24
Nerve cells transmit electric signals through their long tubular axons. These signals propagate due to a sudden rush of Na+ ions, each with charge +e, into the axon. Measurements have revealed that typically about 5.6x1011 Na+ ions enter each meter of the axon during a time of 10 ms. What is the current during this inflow of charge in a meter of axon?

## Slide 25
A typical cost for electric power is $0.12 per kilowatt-hour. (a) some people leave their porch light on all the time. What is the yearly cost to keep a 75-W bulb burning day and night?

## Slide 26
Problem 25.68
What is the potential difference Vad in the circuit?
What is the terminal voltage of the 4 V battery?
A battery with emf 10.3 V and internal resistance 0.5 Ω is inserted in the circuit at d, with its negative terminal connected to the negative terminal of the 8 V battery. What is the difference of potential Vbc between the terminals of the 4 V battery now?